## Slide 1: RCRA Inspector Training
Land Disposal Restrictions
Notes: Welcome to the RCRA Inspector Training on the Land Disposal Restrictions (LDR) Program.

## Slide 2: Introduction
Training objectives
  To strengthen your understanding of the RCRA Land Disposal Restrictions (LDR) program and activities for inspecting facilities for LDR compliance
This training consists of 3 lessons that cover the primary phases of a RCRA inspection
  Lesson 1: Preparing for the inspection
  Lesson 2: Conducting the inspection
  Lesson 3: Conducting follow-up after the inspection
At the end of this training is a final exam
Notes:   This training is designed to strengthen your understanding of the LDR requirements that apply to generators and treatment, storage and disposal facilities (TSDFs), as well as activities for inspecting them. This training assumes that you already have taken the “Fundamentals for RCRA Inspectors” training, which includes an introductory lesson on the LDR program (see Lesson 6).
  The training you will receive today aims to give you a working knowledge of the LDR regulations. Essentially, this means that, by the end of the training, you will be able to determine more effectively if a hazardous waste meets the LDR treatment standards, including the alternative standards (e.g., for contaminated soils). You also will become more familiar with the LDR paperwork that is required of generators and treaters. This training does not focus on less common aspects of the LDR program, such as no-migration petitions or case-by-case variances.
This training is organized into three lessons that cover the primary phases of a typical RCRA inspection. Each lesson focuses on key information that an inspector should know, as well as activities that an inspector may want to perform during that phase of the inspection. For example, Lesson 1 covers preparing for an inspection. In that lesson, we discuss the LDR regulations and describe information to review in preparing for the inspection (e.g., facility permit). In addition, we provide exercises that ask you to prepare for a hypothetical inspection, such as reviewing facility reports.
At the end of the training is a final exam that will evaluate your understanding of the subject matter. If you are taking this training for your RCRA Inspector Certification, you must pass the exam with a 90% score or higher.

## Slide 3: Introduction (continued)
This training has been specially designed to promote increased student interaction and engagement
  Includes numerous exercises that encourage you to apply your understanding of the regulations to resolve compliance problems that may be found in the field
This training is based on the federal RCRA program
  State inspectors should consult their own state’s regulations for requirements that may be more stringent and/or broader in scope
Notes:   This training may differ somewhat in format and design from previous trainings that you have had. Rather than relying heavily on slide presentations to discuss the fundamentals of the RCRA program, this training offers significantly more student exercises to supplement your learning experience; in other words, the training encourages “learning by doing.” The exercises set forth compliance scenarios that you may encounter in the field, followed by one or more questions for you to answer. Most of the time, you will be able to answer the questions based on information provided in the exercise. In a few cases, you will be asked to make an informed guess as to the correct answer; this is perfectly acceptable because you will find out the correct answer in any case. In brief, choose the best answer based on all of the information provided to you.
  The exercises have been developed to strengthen and re-enforce your understanding of the subject matter. Specifically, when you answer a question in an exercise, a pop-up box will tell you whether your answer is correct or incorrect. If it is correct, the pop-up box will explain why it is correct, to validate and re-enforce your understanding. If it is incorrect, the pop-up box will explain why it is incorrect, to strengthen and improve your understanding.
  Keep in mind that, at the end of this training, there is an exam to confirm that you have read and understand the contents of this training, including presentation slides and exercises. Therefore, as you complete each exercise in a lesson, be sure to read the answers in the pop-up boxes fully, irrespective of whether you answered correctly or not. The answers provide important information and are an integral part of this training. In addition, for any incorrect answers, we strongly encourage you to go back and review the relevant requirements in Part 268 before exiting the exercise.

## Slide 4: Lesson 1: Preparing for the Inspection

## Slide 5: Lesson 1: Overview
Welcome to Lesson 1. By the end of this lesson, you will be able to
  Describe the LDR requirements that apply to generators and TSDFs
  Review the LDR regulations to determine the applicable treatment standards for different types of hazardous waste
  Review an LDR notice for compliance with applicable requirements
  Review portions of a RCRA permit to prepare for the inspection
  Review Biennial Report data to find issues that may be relevant to an inspection

## Slide 6: Reviewing the LDR Regulations

## Slide 7: Insert Narration on LDR Regulations

## Slide 8: Insert Part 268

## Slide 9
This notice is being provided in accordance with 40 CFR 268.7 to inform you that this shipment contains waste restricted from land disposal under USEPA land disposal restriction program. Identified below for each container is the designation of the waste as a wastewater or non-wastewater, applicable waste codes and any corresponding subcategories, list of any F001-F005 solvent constituents that are present in the waste, and any underlying hazardous constituents that are present.
Container : NY -189283764658-001 (1/2)
WIP/Approval Code: 800917/PTAAERNJ1
Wastewater or Non-wastewater: Non-wastewater
Waste codes (subcategories): D001 (IGNITABLE CHARACTERISTIC WASTE, LIQUIDS >= 10% TOC PER 261.21(a)(
Constituents (F001-F005): None
UHCs Present: None
Treatment requirements: restricted waste requires treatment to applicable standards
Container :NY -187282764558-002 (2/2)
WIP/Approval Code: 778345/PTAAERNJ1
Wastewater or Non-wastewater: Non-wastewater
Waste codes (subcategories):F002, F003 (NONE), D022
Constituents (F001-F005): Disposal site monitors for constituents
UHCs Present: None
Treatment requirements: restricted waste requires treatment to applicable standards
EPA hazardous waste numbers (i.e., codes), including subdivisions made within a waste code based on waste-specific criteria (such as D003 reactive cyanide)
Land Disposal Restriction Notification Form | 
Generator name: Acme Steel | 
EPA ID number: NY123456789 | Manifest: 000000099 JJK
I hereby certify that all information in this and associated LDR documents is complete and accurate to the best of my knowledge. | 
Signature: | 
Title: Facility Manager | Date: February 14, 2014
The constituents of concern for F001-F005, and F039, and underlying hazardous constituents in characteristic wastes, unless the waste will be treated and monitored for all constituents. If all constituents will be treated and monitored, there is no need to put them all on the LDR notice
The applicable wastewater/ non-wastewater category (see §§268.2(d) and (f))
Notes: Required Information*
Manifest number of first shipment
Statement: The waste is subject to the LDRs
*Based on “Generator Paperwork Requirements Table” at 268.7(a)(4).
Notes: Before moving on, let’s take a closer look at LDR notices because they are an important tool for evaluating compliance. As you may know, there is no standard format for an LDR notice. Waste handlers can determine their format so long as they contain all of the required information. For large shipments or shipments including lab packs, the LDR notice may go on for many pages, and some notices may include accompanying documentation.
The sample notice that you’re looking at was prepared by Acme Steel for wastes that do not meet the LDR treatment standards. Acme prepared the notice in accordance with 268.7(a)(2) and the “Generator Paperwork Requirements Table” at 268.7(a)(4). As you can see, the notice includes information about 2 containers of waste.
At the top of the form is the manifest number of this first shipment of this waste. The manifest number is found in Item 4 of the uniform hazardous waste manifest – in the block titled “Manifest Tracking Number.” Each manifest number is unique, in that each manifest produced or made available to the public must have a unique number.
In addition, for each waste, the notice must include:
-- The applicable wastewater or non-wastewater category. “Wastewaters” are wastes that contain less than 1% by weight total organic carbon (TOC) and less than 1% by weight total suspended solids (TSS). “Non-wastewaters” are wastes that do not meet the criteria for wastewaters.
-- The EPA hazardous waste codes, including subdivisions made within a waste code based on waste-specific criteria (such as D003 reactive cyanide). This notice includes the high TOC subcategory for ignitable waste D001.
-- The constituents of concern for F001-F005, and F039, and underlying hazardous constituents in characteristic wastes, unless the waste will be treated and monitored for all constituents. If all constituents will be treated and monitored, there is no need to put them all on the LDR notice. Note that additional documentation may accompany the notice to describe these constituents, such as a form listing each UHC and describing how the constituent(s) must be managed under 40 CFR 268.7.
-- The notice must state that the waste is subject to the LDRs.

## Slide 10: Insert Lesson 1, Exercise 1

## Slide 11: Insert Lesson 1, Exercise 2

## Slide 12: Reviewing Facility Information

## Slide 13: Inspector Tips to Prepare for Inspection
Re-familiarize yourself with LDR requirements
Review the facility's files (e.g., RCRA permit, enforcement and inspection reports)
  “Permit as a shield” does not apply to LDR requirements unless such requirements are in permit
Review the most recent facility reporting data (e.g., Biennial Report)
  Use the data as a starting point to learn about potential issues
  Recognize the inherent limitations of the data
  Do not accept them on face value
Notes: Adequate preparation is critical to the effective performance of a RCRA inspection.
This slide offers some tips for when you are preparing for an inspection.
In addition to reviewing the regulations, you can refer to applicable guidances and Agency policy (e.g., interpretive letters) to research difficult compliance issues that could arise at the facility.
In the facility’s files, be sure to review the facility’s permit if applicable, past correspondence, as well as enforcement and inspection reports for past or pending violations that need to be followed up on. Keep in mind that permitted TSDFs must comply with the LDR regulations regardless of whether their permit says so (e.g., no placement of waste on the land if it does not meet applicable LDR treatment standards). “Permit as a shield” does not apply to LDR requirements unless such requirements are in the permit.
Consider reviewing EPA or state databases so that you have up-to-date information on the facility, such as the types of wastes generated and received at the facility. This can help you anticipate the types of issues that could arise during your inspection. However, please be aware of the limitations of EPA and state databases (e.g., out-of-date data). Notwithstanding the limitations, the data can be useful for getting an idea of activities taking place at a facility. For example, Biennial Report data could reveal that:
A generator sent lab packs for incineration, but the lab packs contained prohibited constituents (e.g., mercury) in Appendix IV.
A generator sent hazardous waste for incineration, but the waste contained metal-bearing waste listed in Appendix XI.
A facility received offsite wastes that are prohibited in its permit.
These issues might be reflected in data reported on the GM Forms submitted by the generators and/or WR Forms submitted by the TSDFs.

## Slide 14: Inspector Tips to Prepare for Inspection (Continued)
Prepare an inspection checklist that reflects facility-specific information (e.g., its permit)
For permitted facilities, speak with the permit writer
  May be in closer communication with facility than inspectors
  Can discuss facility operations and permit requirements, issues to look for onsite, etc.
  May want to join you during facility visit
Notes: Use your knowledge of the facility to prepare a checklist and plan to guide you during the inspection. Refer to Chapter 5 of the RCRA Inspection Manual for additional information.

## Slide 15: Insert Lesson 1, Exercise 3

## Slide 16: Lesson 1 Summary
Key issues covered in Lesson 1
  Part 268 sets forth treatment standards for hazardous wastes and specifies requirements for generators and TSDFs (e.g., requirements for waste determinations, transmittal of notices/certifications)
  The table in 268.40 sets forth 3 types of treatment standards for hazardous wastes: a “total waste standard,” a “waste extract standard,” and a “technology standard”
  Part 268 also sets forth alternative treatment standards for lab packs, contaminated debris, and contaminated soil
  Inspectors should review available information (e.g., facility permit, past reports, databases) to prepare for the inspection

## Slide 17: Lesson 2: Conducting the Inspection

## Slide 18: Lesson 2: Overview
Welcome to Lesson 2. By the end of this lesson, you will be able to
  Identify potential LDR violations during the facility walk-through
  Review LDR notices for potential compliance problems
  Explain EPA regulations and policy on various aspects of the LDR program (e.g., hazardous debris)
  Review a facility’s LDR treatment results to determine if a waste meets applicable treatment standards

## Slide 19: Inspector Tips for Compliance Reviews of LDR Notices
Are all required elements of the form included fully and accurately?
Are all required waste codes for each waste included?
Is the form signed, if required?
Was supplementary data provided by the generator (if available)?
Is the notice updated when required?
Does the facility retain each form for at least 3 years from the date that the waste that is the subject of such documentation was last sent to on-site or off-site treatment, storage, or disposal?
Notes: In the next several slides, we’ll give you some tips for evaluating compliance with the LDR requirements. After these slides, you will be given an exercise to complete. The exercise will involve some of the inspector tips raised here as well as new ones.
There are many aspects of the LDR Program that an inspector can investigate during the onsite visit. This includes, for example, a facility’s treatment operations (e.g., is the treater treating the waste to meet applicable standards consistently? If some batches failed the standards, why and what measures have been taken to prevent failures in the future?).
Another important aspect of LDR compliance evaluation revolves around the review of facility records. This first slide applies to the review of LDR notices prepared under 268.7 by generators and treaters. When reviewing an LDR notice for compliance, note the following:
--Are all required elements of the form provided? See the Generator Paperwork Requirements Table and Treatment Facility Paperwork Requirements Table for these elements.
--Are all required waste codes provided? The LDR notice should include all waste codes for listed waste and characteristic waste. Note that, where a prohibited waste is both listed and exhibits a characteristic, the treatment standard for the listed waste code operates in lieu of the characteristic code, provided that the treatment standard for the listed waste includes a treatment standard for the constituent that causes the waste to exhibit the characteristic. Otherwise, the waste must meet the treatment standards for all applicable listed and characteristic waste codes. (See 55 FR 22659.) See also the RCRA/Superfund Hotline Monthly Summary (RCRA Online Number 13455).
A helpful practice is to compare the waste codes on the manifest and LDR notice to find problematic discrepancies (e.g., waste codes on the manifest that are not on the LDR notice but should be). In some cases, the waste codes on both forms should be the same. In other cases, there will be justifiable discrepancies. Keep in mind that there are few requirements governing wastes codes that a generator must put on the manifest. Note that up to six waste codes may be included on the manifest, but all waste codes must be on the LDR notice. EPA has clarified that manifest users “should ascertain the waste codes that are most representative of the waste, giving due regard to the degree of the hazardous properties presented (i.e., toxicity, reactivity, ignitability), the waste properties that are most material to the chosen management process, and the volume or relative quantity of the material associated with the waste code in question. We believe it is more practical to rely upon waste handler judgment, rather than develop a rigorous rule that presumes a precise toxicity-based ordering that is neither practical nor credible.” For more information, see 70 FR 10790 (March 4, 2005).
--Is the form signed, if required?
--Is the facility keeping the forms for at least 3 years?
--Was supplementary data provided, such as waste analysis data?
-- Is the noticed updated as required (e.g., when the waste changes)?

## Slide 20: Inspector Tips for Evaluating Generator’s Acceptable Knowledge Determinations
Is published data as current as practicable (e.g., SDSs greater than five years old may be obsolete due to changes in RCRA program, improvements in testing protocols, etc.)?
Do material balances, if used, include the following (among other things):
  Raw ingredient descriptions and physical and chemical properties
  Physical and chemical processes involved prior to and during generation
  Intermediate products
  Materials added and removed during the process?
Notes: This slide discusses tips for evaluating a generator’s use of acceptable knowledge. Under RCRA, generators can use acceptable knowledge or test their waste to make hazardous waste determinations under 262.11 and LDR determinations under 268.7. Acceptable knowledge can include, but is not limited to:
-- Process knowledge, whereby detailed information on the wastes is obtained from existing published or documented waste analysis data or studies conducted on hazardous wastes generated by processes similar to that which generated the waste (process knowledge is supported with technical data);
-- Data from analysis or testing performed by the generator; or
-- In cases of newly listed wastes, data from recent waste analyses performed prior to the effective date of the listings.
For additional discussion of acceptable knowledge, see 58 FR 48111 (September 14, 1993), 59 FR 62916 (December 6, 1994), and 62 FR 62081 (November 20, 1997).

## Slide 21: Inspector Tips for Evaluating Generator’s Acceptable Knowledge Determinations (Continued)
Does the generator review its original acceptable knowledge determination annually, randomly, and whenever the generating process/waste changes or the TSDF finds a nonconformance?
Does the generator understand the potential for changes in the waste and its classification due to environmental factors or spontaneous changes?
Are records kept demonstrating that periodic reviews are being conducted (e.g., a log or certification by facility personnel that is signed annually)?
Notes: This slide, as well as the next one, gives additional tips.

## Slide 22: Inspector Tips for Evaluating Generator’s Acceptable Knowledge Determinations (Continued)
Are analytical results of published studies based on currently acceptable sample/test methods?
Are there significant differences between the published studies and the site’s generation processes/wastes (e.g., raw materials used in the generation process) to warrant concerns about relevancy?
Have you obtained samples of generator’s waste to verify the accuracy of the determinations?

## Slide 23: Inspector Tips for Evaluating Generator’s Waste Analysis Plan (WAP)
For generators treating waste to meet LDR standards in qualified units –
  Do they have and follow a written WAP?
  Is the generator’s treatment appropriate?
  Does the treated waste meet the standards?
  Is the analytical data acceptable?
  Do the data support the generator’s determination?
  Have they done sufficiently frequent sampling given the waste’s variability?
  For non-wastewaters, have they drawn grab samples instead of composites?
Notes:   Inspectors may come across a generator who is treating its hazardous waste in qualified containers, tanks, or containment buildings to meet the LDR standards. The generator must have a waste analysis plan (WAP) in accordance with 268.7(a)(5). An inspector can evaluate compliance by considering the following:
  -- Does the generator have and follow a written WAP?
  -- Is the generator’s treatment appropriate? For example, is the generator using the appropriate type of treatment (e.g., if the treatment method is specified) and is it being performed in conformance with EPA guidance and industry best practices? Is the type of treatment a prohibited type of treatment, such as dilution at 268.3?
  --Does the treated waste meet the standards?
  -- Is the analytical data acceptable? Note that some states require that analyses be done by a certified lab, including analyses done by a generator’s onsite lab. As stated previously, state inspectors should consult their own state’s regulations for requirements that may be more stringent and/or broader in scope than the federal program.
  -- Do the data support the generator’s determination?
  -- Has the generator done sufficiently frequent sampling given the waste’s variability?
  -- For non-wastewaters, has the generator drawn grab samples instead of composites?

## Slide 24: Insert Lesson 2, Exercise 1

## Slide 25: Lesson 2 Summary
Key issues covered in Lesson 2
  Grab samples, not composites, are appropriate for analyzing non-wastewaters under the LDRs
  LDR notices should be reviewed for completeness and accuracy
    Compare the waste codes on the notice to its associated manifest
  Inspectors should review the facility’s treatment results to find potential problems
    Preferably, trending data that show the facility’s effectiveness at meeting the LDR treatment standards over time

## Slide 26: Lesson 3: Conducting Follow-Up After Inspection

## Slide 27: Lesson 3: Overview
Welcome to Lesson 3. By the end of this lesson, you will be able to
  Communicate potential concerns identified during the inspection
  Answer questions raised by stakeholders
  Identify follow-up actions with the facility
  Identify follow-up issues that should be coordinated with other offices

## Slide 28: Insert Lesson 3, Exercise 1

## Slide 29: Lesson 3 Summary
Effective communication is an important aspect of inspection/enforcement process
Sometimes, compliance issues need to be resolved and followed up on after the inspection is done
You should look for issues that may need to be conveyed to others outside of your immediate office
  Other environmental programs
  Permit writer
  Regulated community
  State
Notes: Effective communication within your agency as well as with the regulated community and other regulators is an important aspect of inspection/enforcement process.

## Slide 30: Training Summary
Key issues covered in training
  Part 268 sets forth treatment standards for hazardous wastes and specifies requirements for generators and TSDFs (e.g., requirements for waste determinations, transmittal of notices/certifications)
  The table in 268.40 sets forth 3 types of treatment standards for hazardous wastes: a “total waste standard,” a “waste extract standard,” and a “technology standard”
  Part 268 also sets forth alternative treatment standards for lab packs, contaminated debris, and contaminated soil
  LDR notices should be reviewed for completeness and accuracy

## Slide 31: Training Summary (Continued)
  Inspectors should review the facility’s treatment results to find potential problems
    Preferably, trending data that show the facility’s effectiveness at meeting the LDR treatment standards over time
  Inspectors should evaluate 1) a facility’s compliance with its permit as well as 2) the permit requirements themselves
    Inspection may uncover deficiencies in the permit that require further action to resolve

## Slide 32: Summary of Key Inspector Tips
Prepare in advance for the inspection (e.g., review the permit files, re-familiarize yourself with the regulations)
During onsite inspections:
  Review LDR notices for compliance (e.g., are all required elements of the form included fully and accurately?)
  Review generator’s acceptable knowledge determinations and facility implementation of waste analysis plans
  Use performance-based inspection of facility to thoroughly identify and evaluate waste generation and management
  Evaluate the inter-relationships among the various facility operations and how they could affect each other from a compliance standpoint (e.g., upstream operational problems causing downstream compliance problems)

## Slide 33: Summary of Key Inspector Tips (Continued)
After the onsite inspection, communicate with stakeholders (e.g., permit writer, other agencies, state)

## Slide 34: Resources
“Introduction to Land Disposal Restrictions” http://www.epa.gov/osw/inforesources/pubs/training/ldr05.pdf
“Land Disposal Restrictions: Summary of Requirements” http://www.epa.gov/osw/hazard/tsd/ldr/ldr-sum.pdf
“Guidance on Demonstrating Compliance With the Land Disposal Restrictions (LDR) Alternative Soil Treatment Standards”
http://www.epa.gov/osw/hazard/tsd/ldr/soil_f4.pdf

## Slide 35: Resources (Continued)
“Waste Analysis At Facilities That Generate, Treat, Store, And Dispose Of Hazardous Wastes” http://www.epa.gov/osw/hazard/tsd/ldr/wap330.pdf
EPA memo regarding the placement of prohibited wastes (i.e., wastes that do not meet LDR treatment standards) in a landfill (RCRA Online Number 14843; 4/11/14) http://www.epa.gov/solidwaste/inforesources/online/index.htm
Fundamentals for RCRA Inspectors Training
  www.epa.gov/compliance/training/neti/index.html

## Slide 36: Resources (Continued)
Process-Based Inspections Training
  www.epa.gov/compliance/training/neti/index.html
RCRA Inspection Manual